## Slide 1: Ice Scouting CubeSat ISCube
Josiah Delange, Seth Merrifield, Thomas Georgiou,
Alec Forsman, Yunus Agamawi, Haley Rorvick,
John Jackson, Keegan Clay

## Slide 2: Agenda Josiah DeLange
Overview
Approach
Project Plan and Budget
Design Walkthrough
FMEA and Safety Analysis
Standards
Conclusion
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 3: Overview Josiah DeLange
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Mission Goals
Remotely detect water with a 6U CubeSat
Characterize energy spectrum of gamma ray photons
Supplement a broad range of envisioned deep space missions
[e.g. asteroid scouting, interplanetary reconnaissance, long-range sample return]
Implied Requirements
Compact, low-power, low-cost
Detection accuracy sufficient for relative navigation
Ability to relay payload information to other spacecraft
6U deployment mechanism

## Slide 4: Overview
Data Acquisition
Neutron spectrum
Gamma-ray photon spectrum
Radiation background
Power Control
Communication / Data Relay
Orbital Trajectory
Propulsion
Attitude Control
On-board Processor
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Josiah DeLange
Navigation E.K.F. State Vector
x(t) = [r v]T
x(t) = f(x(t),t) + u(t)

## Slide 5: Motivation
Companies interested in asteroid mining
  Planetary Resources
  Deep Space Industries
Detect valuable resources for future missions
  Minerals
    Rare Metals
    Structural Materials
    Gases
  Water - primary goal
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 6: Motivation
Protection from solar radiation
Sustain life systems
  Breathable air
  Hydration
Facilitates the mining of other materials
  High mass ratio payback
Can be converted into fuel propellant
  Cost to bring water from surface of Earth to space = $23,000/lb
  Estimates for water-rich(~8%), 500m wide asteroid
    80 times more water than the worlds largest supertanker
    200 times the rocket fuel required to launch all rockets in history
    Net worth of $50 Billion - conservative estimate
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 7: Requirements Josiah DeLange
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Navigation accuracy of one kilometer
  DSN’s accuracy is one kilometer
  Goal is to supplement + mitigate DSN loss
Photon binning down to 0.1 us
  Enables the navigation accuracy of one kilometer
Distance of 0.5 km from 2009 BD
  Enables sufficient SNR for detection
Internal payload temperature between 0 and 40 oC
Mass limit of 12 kg
Dimensional limits of 12x24x36 cm
CubeSat design restrictions
Radiation tolerant components

## Slide 8: Project Approach
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 9: Approach
Main goal: acquire meaningful data
  Subsystems to facilitate goals
Off-the-shelf
  Goal to focus on mission, not subsystem hardware
Power-centric
  Fundamental to nano-satellite design
Industry and faculty support
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Seth Merrifield

## Slide 10: Project Plan and Budgets
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 11
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 12: Project Budget | Full
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Subsystem | Equipment | Cost
Navigation/ Communication | S-Band Transceiver, S-Band Patch Antenna | $21,000
Propulsion | CubeSat Ambipolar Thruster | $30,000
Power | Solar Panels, Batteries | $55,400
Attitude Determination | iADCS-100 | $40,000
Detection | Photodiodes, Borated Plastic, Lithium Glass, Pulse Processor | $2,000
Thermal | MLI, Thermal Conducting Pads | $700
Structural | 6061-T6 Aluminum (various dimensions) | $100
Total CubeSat Materials Cost:
$149,200
Compared to Large Satellite Cost:
$250 million
Haley Rorvick

## Slide 13: Schedule | HASP Build Components
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Gamma ray detector
1-U Solar panel characterization
Arduino writing to SD card
  4 different setups
  How does shielding against radiation affect it?
Similar design challenge to actual CubeSat
Tasks to be assigned
John Jackson

## Slide 14
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
John Jackson

## Slide 15: Project Budget | HASP Build
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Equipment | Price
Arduino Uno (5) | $125
SD Card Shield (5) | $75
1-U Solar Panel | $2250
Wires and connectors | $30
Detector Material | $2000
Total | $4480
GPS donated by NavCom. Other materials needed will be procured with the assistance of Seth Frick, project manager, and our faculty and industry partners.
John Jackson

## Slide 16
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Yunus Agamawi

## Slide 17: Design Walkthrough
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 18: System Overview
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Basic System Information
CAN bus for inter-sensor communication
Power regulated and delivered from PRC
FCM hands off commands and performs calculations
John Jackson
32-bit uC Flight Computer

## Slide 19: CAD Model Overview
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
S-Band Patch Antenna
ADCS
Fuel Tank
Thruster
S-Band Patch Antenna
S-Band Transceiver
Batteries
Processor(s)
Detector
Haley Rorvick

## Slide 20: Finding Water
Spectral Analysis
Emitted radiation contains traces of known elements
Neutron/gamma interaction (neutrons suggest water ice)
Presence of gamma radiation
“Fast” neutrons (~ 1 MeV)
Interact with hydrogen-rich materials
Use organic plastic material to detect
Wavelength for max emission: ~430 nm
“Thermal” neutrons (~0.025 eV)
Interact with isotopes of lithium
Use lithium-doped glass material to detect
Wavelength for max emission: 386 nm
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Josiah DeLange

## Slide 21: Typical Counter Setup: Photomultiplier Tube
R
R
R
R
Dynodes
Anode
High-energy
particle
Scintillator
Photocathode
1 electron
106 electrons
VB
“Dynode Chain” PMT
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Josiah DeLange
Notes: Initial electron is accelerated toward first dynode (high bias voltage induces electric field)
Additional electrons produced due to electron avalanche process
Etc; resulting gain of roughly 106
Pros
Ideal for small signals, i.e. single particle detection
Resulting electric signal is sufficiently amplified
Cons
Physical size (larger PMTs require a higher bias voltage)
Sensitivity to magnetic fields
Power requirements

## Slide 22: Small Counter Setup: Avalanche Photodiode
High-energy
particle
Scintillator
N
P
P+
depletion region
1 electron
106 electrons
Light Pulse
hole
Anode
Cathode
Reflective PTFE tape
Aluminum Housing
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Josiah DeLange

## Slide 23: Wavelength Matching
Lithium-Glass
BC-454 Plastic
S8664 APD
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
http://www.apace-science.com/ast/g_scint.htm
http://www.crystals.saint-gobain.com/uploadedFiles/SG-Crystals/Documents/SGC%20BC454%20Data%20Sheet.pdf
http://www.hamamatsu.com/resources/pdf/ssd/s8664_series_kapd1012e04.pdf
Josiah DeLange
Notes: FIGURES:
Left: http://www.apace-science.com/ast/g_scint.htm
Middle: http://www.crystals.saint-gobain.com/uploadedFiles/SG-Crystals/Documents/SGC%20BC454%20Data%20Sheet.pdf
Right: http://www.hamamatsu.com/resources/pdf/ssd/s8664_series_kapd1012e04.pdf
Spectral ranges of emission must coincide for any of this to work
Regions of overlap determine approximate shape of the energy spectrum

## Slide 24: Particle Discrimination
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Lithium-Glass
Borated Plastic
Fast Neutrons
Thermal Neutrons
Josiah DeLange
80 MHz ADC clock
12 bit ADC
4 MHz count rate
Peak time of 0.2 us
Notes: Expect a more grainy, continuous spectrum from the BC-454 detectors; due to a lot of thermal particles and also they are plastic (thus lack resolution)
Expect more distinct peaks from the lithium-glass detectors, as the particles they sense are very high energy

## Slide 25: Detector Energy Resolution
NaI(Tl) Detectors
Organic Plastic Detectors
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Josiah DeLange
Notes: FIGURES:
Left: Thorium-232 source, detected using inorganic crystal (NaI(Tl)) detectors; 2048 bins
Right: Thorium-232 source, detected using organic plastic (BC-412) detectors; 1024 bins
No energy levels, just bins, although calibration can be followed through easily with this kind of data
Compare resolution and detectable range of energy for different detector materials

## Slide 26: Orbits, Propulsion, Attitude
Orbital Determination
ADCS
Propulsion
Seth Merrifield
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 27: Asteroid Selection
Key: non-monolithic ->
2009 BD
  10 m, 80000 kg
  a = 1.015 AU
  H=28.1
  ⍵ = 0.005 r/s
Asteroid Itokawa, visited by Hayabusa probe in 2005
http://www.isas.jaxa.jp/e/snews/2005/1102.shtml
Seth Merrifield
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 28: Basic Orbit Determination
Target asteroid: facilitate mission outcome
  minimize: time of mission, ΔV
  largest potential asteroid from given list
http://ssd.jpl.nasa.gov/sbdb.cgi?sstr=2009%20BD;orb=1
Seth Merrifield
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 29: Propulsion : PEPL Ambipolar Plasma Thruster
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Designed specifically for this type of mission
Continuous or Pulsed Thrust (2mN vs 20mN thrust)
Exit Velocity = 20,000 m/s
Fuel Required ≈ 2.5 kg [Xe]
Operating Power ~10W
Size ~2U (with fuel)
Still in development
http://pepl.engin.umich.edu/thrusters/CAT.html
Notes: Design of propulsion not in scope of project → pick off the shelf option
Plasmadynamics and Electric Propulsion Laboratory - University of Michigan
thruster technology will be able to send low-cost satellites from the Earth to go observe and radio-tag asteroids for retrieval
run continuously at periapsis for certain number of degrees or pulse it around periapsis

## Slide 30: Attitude Determination & Control Requirements
Velocity Vector Stabilization & Accuracy
< 5° between long axis and velocity vector (95% confidence)
No requirement for roll angle
Velocity Vector Attitude Knowledge
Measure attitude within +/- 1° at the time of receiving data
De-Tumble & Tip-Off Recovery
Recover from tip-off rates up to ~100°/s
Stabilize within 2 days
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Off-the-shelf iADCS-100 chosen
3-axis reaction wheels/magnetorquers
3-axis accelerometers/magnetometers
Star-tracker, gyro
www.berlin-space-tech.com
Notes: Velocity Vector Stabilization
Because optimal control law angle found to be ~5deg outward, choose < 5 deg accuracy
De-Tumble
T_req = 0.0502 mN
T_iADCS = 0.087 mN

## Slide 31: Subsystem Relationships
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Modes of Operation
C&DH - May at any time force the ADCS into any state or reboot
Notes: Subsystem Relationships
Command and data handling system
Transfer Orbit
Initialization - Power supplied for ADCS is supplied. Sensors and actuators are initialized.
Failsafe - ADCS remains on standby until a command from the CHDS allows it to continue to de-tumbling mode.
De-Tumbling - ADCS will de-tumble the satellite. Once complete or not necessary, system continues to Power Safe mode
Power Safe - Attitude of the satellite and deployable solar panels oriented to obtain the maximum power input. Power consumption kept low when satellite is in the shadow of Earth.
Optimal Thrusting - Orient long axis to optimize thrust direction
At Asteroid
Detector Pointing - Change attitude to acquire optimal orientation of detectors for spectroscopy for given time (hour at least)

## Slide 32: Tip-Off Recovery
Problem : Tip-Off Rate Recovery Rate
Approach : Use maximum moment of inertia to determine the torque of fly-wheels required to stabilize
From simplified analysis, iADCS-100 flywheel torque capability should suffice.
Next step - 3D moments with mass distribution accounted for.

## Slide 33: Velocity Vector Stabilization
Problem : Optimizing thrust vector
Approach : Derive the equations of motion and develop MATLAB model
Solutions : Develop optimal torque control law to stabilize thrust vector
Conclusions :
  Non-trivial solution
  Optimal direction of thrust ≈ 5° from perpendicular
  Deviation from optimal direction becomes significant at ~ 5-10°
    This determines required accuracy of velocity vector desired
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Notes: non-trivial solution: depends on
the mass of the cubesat
the maximum thrust capability
Optimal direction of thrust kept at 5deg from perpendicular
T is proportional to the difference from the angle being 90degrees
attenuation term phidot, to provide damping to the oscillations

## Slide 34
Notes: Orbital time = 1year
10deg outward from optimal thrust → 3.5% decrease of reach
10deg inward from optimal thrust → 2% decrease of reach
Therefore an accuracy of 5deg

## Slide 35: Result of Orbit Determination: Step 1
Seth Merrifield
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 36: Result of Orbit Determination: Step 2
Seth Merrifield
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 37: Result of Orbit Determination: Step 2
Seth Merrifield
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 38: Result of Orbit Determination: Step 3
Seth Merrifield
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 39: Navigation
Orbital Path Trajectory
  Verification
  Correction
Asteroid Rendezvous
Primary Means
  Deep Space Network (DSN)
    Differential One way Ranging
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
http://timeandnavigation.si.edu/multimedia-asset/navigation-in-space
Yunus Agamawi

## Slide 40: Navigation
Gamma-ray source Localization-Induced Navigation and Timing (GLINT)
Interplanetary Network (IPN)
Gamma-ray Burst Coordinate Network (GCN)
Gamma-Ray Burst Detector
  20keV to 3MeV
“Spacecraft Navigation Using Celestial Gamma-Ray Sources”, Chuck S. Hisamoto and Suneel I. Sheikh, AAS Paper 13-144,Advances in the Astronautical Sciences, Proceedings of the 23rd Space Flight Mechanics Meeting, Kauai, HI, Vol. 148, 10-14 February 2013, pp. 3903-3922.
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Yunus Agamawi

## Slide 41: Navigation
High precision onboard clock
  Resolution of photon binning
Autonomous navigation and processing capabilities
  Remote computation of telemetry path
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
“Spacecraft Navigation Using Celestial Gamma-Ray Sources”
Yunus Agamawi

## Slide 42: Communication
Transmit sensor findings
  Scouting asteroid
Update Navigation Solution
  Deep Space Network
    Monitoring CubeSat
  Nearby Spacecraft
    Gamma Ray Burst Almanac
      Time of Arrival
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
“Spacecraft Navigation Using Celestial Gamma-Ray Sources”
Yunus Agamawi

## Slide 43: Communication
SWIFT-SLX: S-Band Transceiver (Tethers Unlimited)
  Bandwidth communicating over DSN
  Meet link budget range requirements
S-Band Patch Antenna (Surre Satellite)
  Uplink/Downlink capabilities
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Yunus Agamawi

## Slide 44: Thermal Control
Operating Temperature Requirements
Haley Rorvick
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Subsystem | Components | Operating Temperature
Navigation | Antenna and Transceiver | -20℃ to 50℃
Detection | Photodiodes | -20℃ to 50℃
Detection | Lithium Glass/ Borated Plastic/ Sodium Iodide Crystal | <375℃
Detection | Amplifier Chip | -55℃ to 125℃
Attitude Determination | iADCS-100 module | -20℃ to 40℃
Propulsion | Ambipolar Thruster | N/A
Power | Batteries | 0℃ to 50℃
Power | Solar Panels | 0℃ to 115℃
Required Internal Temperature Range
0℃ to 40℃

## Slide 45: Thermal Control Space Environment and Thermal Control Components
Passive Thermal Systems
MLI (Multi-Layer Insulation)
  protects against unwanted heating or cooling
Thermal Fillers
  Promotes conduction between various electronics and to surface radiators
Solar Panels
  Silicon Solar Cells w/ 3mm of glass
  Solar panels will keep surface temperature at approximately 20°C
Thermal Properties of Space
Direct Exposure to Sun: Temperature ≈ 115°C
Based on the orbital path, the CubeSat will be mostly in the sun
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Multi-Layer Insulation
Haley Rorvick

## Slide 46: Thermal Control
Thermal Gap Filler (AOK)
Electrically Insulating
Good Thermal Conductivity (0.8 W/m-K)
Naturally Tacky
Continuous Use Temp: -40℃ to 150℃
Thickness: 5mm to 12mm
* In order to conduct testing, arrangements have been made with the company for free samples
Haley Rorvick
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 47: Thermal Control
Multi-Layer Insulation
Conductive heat path is minimized by alternating Layers of Aluminized Mylar and Polyester veil
Number of Layers: 15
Effective Emittance: ~0.003
Verified by NASA research
MLI is extremely sensitive and can break easily
Haley Rorvick
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 48: Power
Most fundamental requirement for any spacecraft
Determining the proper power system
  Length of mission
  Power needed
  Feasible
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Alec Forsman
Notes: Insert picture of determining power systems

## Slide 49: Solar Array Sizing
Determining power consumed
Consumption is not always equal to production
  Array Regulator
  Power Control and Distribution Unit (PCDU)
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Component | Power Consumption (W)
S-Band Patch Antenna | 10
SWIFT-SLX: S-band SGLS/USB/ISM Transceiver | 8.7
iADCS-100 | 1.8
CubeSat Ambipolar Thruster | 10
Detector System | 6
Battery Recharging | 23.35
Total Power | 59.85 (~60)
Alec Forsman
Notes: edit figure
Area equation, what affects power produced, what we’ll be operating in, potential concerns

## Slide 50: Solar Array Sizing
Factors Affecting Array Sizing | Value
Power Needed (Parray) | 60 W
Solar Flux (S) | 1270 W/m2
Array Pointing Accuracy (δθ) | 1°
Solar Cell Efficiency (ηcell) | 29 - 0.08T
Cell Packing Efficiency (ηpacking) | 0.90
Array Degradation Factor (D) | 0.20
Temperature (T) | 0-115°C
Array Size: 3315 cm2
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Alec Forsman
Notes: insert graph

## Slide 51: Solar Array Sizing
Arrangement on CubeSat
  Solar panel area: 3315 cm2
  Area of 6U: 3168 cm2
  Effective Area: 1815 cm2
    Angle of sunlight irradiance: Ψ = 35°
  Area of deployed solar panels: 1500 cm2
    Area of single deployed panel: 750 cm2
      w ~ 20 cm & l ~ 37.5 cm
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Alec Forsman

## Slide 52: Off the Shelf Options
Clyde Space
  6U panel array
Offer customization option
Technical Readiness Level: 2
Single wall panel for a 6U CubeSat
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Alec Forsman

## Slide 53: Batteries
Need to supply power in Earth’s umbra
  Determined by the period of eclipse
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Alec Forsman
Notes: Picture of clyde space battery (x)
determined by eclipse time, equation to det bat enegy, clyde space bat 30whr, potential problems(cycle life)

## Slide 54: Battery Sizing
Max time spent in eclipse: ~1.867 hr
(EB)max= 85 Whr
  ηcharge = 95%
  DOD = 70%
3 x 30Whr needed
  Clyde Space
30 Whr standalone battery offered by Clyde Space
Alec Forsman

## Slide 55: Battery effects on Power
Need to be able to recharge the batteries
Max power needed
  ~23.65 W
Alec Forsman

## Slide 56: Radiation Background
Earth Radiation Zone - Van Allen Radiation Belt
  Inner Belt - proton dominated
  Outer Belt - electron dominated
Auroral Zone
  Low energy electrons
  Low percentage of protons
Interplanetary Zone
  Solar wind
    Continuous ejection of protons and electrons
  Solar flares
    Large flares - extremely rare
    Small flares - occur approximately 8 times a day
  Cosmic flux
    Originate from supernovae, active galactic nuclei and gamma ray bursts
Alec Forsman

## Slide 57: Radiation Effects
Degradation of internal components
Degradation of solar array performance
  Displacement damage
  UV exposure darkens cover glass
    Decreases Illumination & increases operating temperature
Single-event upsets
  Produces false commands
Dielectric charging
Embrittlement
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Alec Forsman

## Slide 58: Radiation Protection
Internal Components
  Radiation Hardening
  Shielding from aluminum structure and solar panels
Solar Array
  Increase cover glass thickness
  Reduction in energy conversion efficiency is inevitable
    Design for this (EOL)
      Array degradation factor (D)
Alec Forsman

## Slide 59: FMEA and Safety
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 60: FMEA and Safety | FMEA Overview
Total FMEA elements : 132
Critical subsystem FMEA elements:
Propulsion
Power
Mission Orbit
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
John Jackson

## Slide 61: FMEA and Safety | Top FMEA Elements
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Subsystem | Failure mode | Probability | Severity | CON
Orbital | orbital transfer miscalculated | 4 | 10 | 40
Power | End of Life (EOL) not designed high enough | 5 | 8 | 40
ADCS | Reaction Wheel Fails | 4 | 10 | 40
Power | Cell failures occur | 6 | 6 | 36
Orbital | engine does not perform at expected level | 5 | 7 | 35
Power | Mission takes longer than expected and solar panels degrade | 5 | 7 | 35
Power | Solar panels cant produce enough power for mission duration | 4 | 8 | 32
John Jackson

## Slide 62: FMEA and Safety | Safety Concerns
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Care needs to be taken with propulsion
Propulsion unit, solar panels
Possibility of collision with other spacecraft
  nature of orbit leaving Earth
Need to coordinate with appropriate agencies to minimize risk
  NASA, ESA, etc.
John Jackson

## Slide 63: Appropriate Standards
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 64: Appropriate Standards | CubeSat Design
CubeSat Design Standard - Cal Poly
Regulates design of 1-U to 3-U CubeSats
Larger CubeSats being explored for the future
Deviation Waiver Approval Request
Required if some design specs are different
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
John Jackson

## Slide 65: Appropriate Standards | Procedure Standards
NOAA Remote Sensing License
Required for non-government remote sensing spacecraft
LSP Program Level P-POD and CubeSat Requirements Document (LSP-REQ-317.01)
NASA’s requirements for P-POD launcher
General Environmental Verification Standard for GSFC Flight Programs and Projects (GSFC-STD-7000)
System and environment testing for space systems
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
John Jackson

## Slide 66: Appropriate Standards | Procedure Standards
Military Standard Test Requirements for Launch, Upper-stage, and Space Vehicles (MILSTD-1540)
In-depth procedure on environment and system verification
Air Force Space Command Manual 91-710, Range Safety User Requirements Manual (AFSPCMAN 91-710)
Guidelines for safety and minimum design requirements for safety-critical missions
Standard Materials and Processes Requirements for Spacecraft (NASA-STD-6016)
Minimum requirements for NASA spacecraft materials and processing
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
John Jackson

## Slide 67: Appropriate Standards | Procedure Standards
NASA Procedural Requirements for Limiting Orbital Debris (NPR 8715.6)
Guidelines on minimizing space debris production
NASA Procedure for using DSN, SN
To communicate with spacecraft
Many, many others
Standard modelling practices, environmental standards
Navigation radio standards
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
John Jackson

## Slide 68: Conclusions
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions

## Slide 69: Conclusions
Subsystem Technical Readiness Level:
Detection: 4
Processing: 2
Propulsion: 2
Communication: 2
Power Control: 2
Mission Technical Readiness Level:
2
Overview | Approach | Project Plan | Design Walkthrough | FMEA and Safety | Standards | Conclusions
Alternative hardware to consider:
External optical sensors
Ranging device
[laser rangefinder]
Solid-state radiation detectors
Different detector geometries

## Slide 70: Life Long Lessons
Adhering to a strict schedule
Communication is key
The engineering process is a while(1) loop
  Converge on a solution
Have to learn to accept certain standards
  There most likely isn’t a right answer
  There will always be room for improvement
Time is your most valuable resource
Alec Forsman

## Slide 71: Individual Design Contributions
Feasibility assessment
  Power, mass, size
  Are we even close?
Power
  Designed Solar Panels from the ground up
  Batteries needed
Radiation
  Determined the effects
  Found ways to minimize damage
Alec Forsman

## Slide 72: Formulating Requirements
Solar Panels:
Power vs. Solar Panel Area
  Infinite area = Infinite power
Accurate estimation of parameters
Choosing what environment to model
  Interplanetary
  LEO
  GEO
Can we survive a worst case scenario?
Alec Forsman
Batteries:
Power they need to produce
Amount of time in eclipse
Number of batteries needed
  Worst case was 9
Can they be recharged?

## Slide 73: Engineering Methodology
Alec Forsman

## Slide 74: Engineering Methodology
Use Matlab to

## Slide 75: Individual Design Contributions
Propulsion:
  Researched available propulsion to determine adequate thrusters for mission
    Busek, Clyde Space, PEPL, NASA, ESA
  Wrote MATLAB function to approximate fuel required/consumption
Orbit :
  Developed MATLAB model of planar orbit to determine ADCS specifications
    Velocity Vector / Tip-Off Recovery
    Determined optimal thrust vectoring through iteration
ADCS :
  Researched available ADCS to be able to meet mission specifications
    Torque capability → Tip-Off Recovery Time
    Developed understanding of sensitivity through simulation
Notes: Addressed issues in several areas

## Slide 76: Thomas - Ability to formulate Design Req.
Thruster requirements based on:
  Size
  Fuel consumption for mission
ADCS requirements based on:
  Velocity vector accuracy
    developed from analysis of MATLAB orbital model
  Actuator torques

## Slide 77: Engineering Methodology: Fuel Required
Tsiolkovsky Rocket Equation
For PEPL Ambipolar Thruster
Assumes impulsive maneuver
Ignores friction from Earth’s atmosphere

## Slide 78: Engineering Methodology: Actuator Requirements
From simplified analysis, iADCS-100 flywheel torque capability should suffice.
Next step - 3D moments with mass distribution accounted for.

## Slide 79: Engineering Methodology: Planar Orbit Simulation
Using the Lagrangian
Torque control law:
optimized to maximize orbit reach through iteration

## Slide 80: Thomas - Lessons Learned

## Slide 81: Thomas - Lessons Learned
Timing
Direction is crucial
Importance of Planning
Problem Solving & Persistence
Notes: Get things done on time, especially when others depend its completion
Knowing where a project is headed is crucial to doing good/productive work

## Slide 82: Individual Design Contribution
Navigation Systems
  Deep Space Network
  Navigation Aid
Communication Systems
  Relaying Data/Commands
  Mission Control
  Sensor findings
Total Hours: 72
Yunus Agamawi

## Slide 83: Specific Design Requirements
Navigation Aid
  Detection system
Transmit/Receive Data
  Relay sensor findings
    Transmitter/Antenna Power
  Navigational information
  Mission Commands
    Receiver/Antenna Power
Yunus Agamawi

## Slide 84
Yunus Agamawi
http://eecue.com/a/1581/Goldstone-NASA-Deep-Space-Network.html
http://en.wikipedia.org/wiki/Global_Positioning_System

## Slide 85: Equivalent Isotropic Radiated Power, EIRP
PT - transmission power
  0dB
LT - transmission loss
  1.5dB (LEO satellites)
GT - transmission antenna gain
  8dB
Yunus Agamawi
EIRP = PT – LT + GT
EIRP = 0dB - 1.5dB + 8dB
EIRP = 36.5dBm
http://www.space.aau.dk/cubesat/galleri1.html

## Slide 86: Propagation Losses, Lprop
FSL - Free Space Loss
  246dB (0.15AU range)
Labs - Atmospheric Absorption
  0.1dB (precedence)
Lpol - Polarization Loss
  3dB (precedence)
Laml - Antenna Misalignment Loss
  1dB (precedence)
Yunus Agamawi
Lprop = FSL + Labs + Lpol + Laml
Lprop = 246dB + 0.1dB + 3dB + 1dB
Lprop = 250.1dB
http://www.aboutcivil.org/sources-of-errors-in-gps.html

## Slide 87: Link Budget: Received Power, PR
EIRP – Equivalent Isotropic Radiated Power
  36.5dBm
Lprop - Propagation Loss
  250.1dB
LR - Receiver Loss
  1.5dB (analogous to transmitter loss)
PR = EIRP - Lprop - LR
PR = 6.5dB - 250.1dB - 1.5dB
PR = -244.9dB
http://www.spacetoday.org/SolSys/DeepSpaceNetwork/DeepSpaceNetwork.html
Yunus Agamawi

## Slide 88: Link Budget: Carrier to Noise, C/N
PR - Power Received
  245dB
GR - Receiver Gain
  85.9dB
C/N = PR + GR - TS - k
C/N = -244.9dB + 85.9dB - 18.8dBK + 228.6dB/K/Hz
C/N = 50.6dB
TS - System noise temperature
  18.8dBK (precedence)
k - Boltzmann constant
  228.6dB/K/Hz
Yunus Agamawi

## Slide 89: Link Budget: Downlink Margin
BitRate – bit frequency
  1/9600 Hz ≈ -40dBHz
Eb/N - Energy per bit to noise
Downlink Margin = Eb/N + BER
Downlink Margin = 10.6dB - 9.6dB
Downlink Margin = 1dB
Eb/N = C/N + BitRate
Eb/N = 50.6dB/Hz - 40dBHz
Eb/N = 10.6dB
BER, Bit Error Rate
For less than 10-5 errors
  BER = -9.6dB
Yunus Agamawi

## Slide 90: Link Budget: Uplink Margin
Yunus Agamawi
EIRPS = 56dB - 1.5dB + 85.9dB = 140.4dB
LPROPS = 246dB + 0.1dB + 3dB + 1dB = 250.1dB
PRS = 140.4dB - 250.1dB - 1.5dB = -111.2dB
C/NS = -111.2dB + 8.0dB - 18.8dBK + 228.6 dB/KHz = 106.6 dB/Hz
EB/NS= 106.6dB/Hz - 40dbHz = 60.6dB
Uplink Margin = 60.6dB - 9.6dB = 51dB

## Slide 91: Life–Long Learning
Turning big, hairy, audacious goal into smaller, conquerable tasks
Defining roles and accountability evenly between members
Yunus Agamawi
http://www.daimanuel.com/my-super-top-secret-hack-that-accelerates-your-fitness-goals-that-works-nearly-every-single-time/

## Slide 92: Life–Long Learning
Assessing team member strengths
  Delegating responsibilities accordingly
Recognizing and handling unexpected issues and complications
Yunus Agamawi
http://blog.bluechipcommunication.com.au/wp-content/uploads/2012/09/

## Slide 93: Seth - Life Long Learning
Aerospace/Technology
  Remote Sensing, propulsion, asteroids...
Professional development
  Teamwork, teamwork, teamwork
    team integration
    prioritization and time management
    working mindfully
    communicating effectively
http://www.asterank.com/3d/

## Slide 94: Seth - Individual Design Contributions
Address broad concerns about mission architecture
  Independent CubeSat or fleet with mothership?
    Is a transfer possible with a CubeSat?
      Engine? Targets?
    If not, what kind of mothership do we use?
ETC…
Given assumptions, is this project possible?
Seth Merrifield

## Slide 95: Design Contribution
Approach: research, research, model, repeat
  U Mich PEPL Lab, NASA, ESA, Busek, STK
Relevance: proof of concept
  No project without asteroid, no asteroid without engine
Results: feasibility assessment, illustration
  Use STK to look at orbits and see if they work
  Illustrate design concepts
  Insight into process for potential test flight planning
Seth Merrifield
Notes: Your goal is to explain what you did, how you did it, why it was important to the overall project, and how it turned out. Report any significant effort even if the results were NOT used in the final design. Design studies not used are still valid work and should be presented. It may be necessary for team members to repeat some material that is common to your individual work. Try to minimize this but some repetition will be tolerated

## Slide 96: Seth - Ability to formulate Design Requirements
Estimate minimum ΔV using Kepler’s Equations
Research engine technology to select promising candidates
use STK to model mission using selected engine
  create engine model
  use JPL data to create SPICE file for STK
Seth Merrifield

## Slide 97: Seth - Engineering Methodology
Estimate orbital transfer requirements
  back of the envelope estimates to start
    inform propulsion decision making
    help decide on asteroid
Determine feasibility
  CubeSat transfer parts
    leave SOI
    change orbit around sun to match asteroid
      importance of epoch
    chase asteroid
Seth Merrifield

## Slide 98: Seth - Engineering Methodology
STK custom propulsion modelling
  Also: Space Effects and Environment Tool (SEET), solar flux, performance over time, model articulation, radiation pressure, comm-systems
Making educated guesses
  initializing STK model
  formulating general mission procedure
STK for heavy lifting/calculation
  Propagators: Astrogator, HPOP, Heliocentric
  JPL Horizons: SPICE files for asteroid data
Seth Merrifield

## Slide 99: Optimization
Seth Merrifield

## Slide 100: Optimization
Seth Merrifield

## Slide 101: Example STK report - sun illumination times
Seth Merrifield

## Slide 102: STK report: solar intensity over time
Seth Merrifield

## Slide 103: Life Long Learning
Requirements, requirements, requirements
The chicken and the egg
Project suffered from lack of
Relationship Dynamics
Frustration is cumulative
Project Strategy
“Get your work done”
Time is Precious
Documentation
John Jackson

## Slide 104: Individual Design Contributions
Project Strategy
Pushed to define requirements early
Tried to keep us on track
Provided literature - Space Systems Engineering
System Architecture Overview
Subsystem breakdown
System modelling
Began ADCS Modelling
CDR Planning
FMEA and Standards
Next semester proposal and build plan
John Jackson

## Slide 105: Design Requirements
CubeSat Standards
No 6-Us currently launched
Certain mass and geometry constraints
Spring Semester Build
Adapt our project for HASP requirements
John Jackson

## Slide 106: Engineering Methodology
Engineering References
Spacecraft Systems Engineering 4th
Previous / current CubeSat missions
ARKYD testbeds
Simulation in Simulink
Writing on a whiteboard
John Jackson

## Slide 107: Lifelong Lessons
Importance of openness
Tell everyone what you did (and why)
Tell everyone what you didn’t do (and why)
Important social conventions
High-quality work follows from continued peer recognition
Interpersonal skills can make or break a team’s cooperation
Meetings as a way to communicate (but not simultaneously)
Miscellaneous
Clear, logical objectives
Positive attitude despite setbacks
Accepting disagreement as being useful for progress
Create enthusiasm and initiative
Josiah DeLange

## Slide 108: Individual Design Contributions Josiah DeLange
Lithium-Glass
Borated Plastic
Fast Neutrons
Thermal Neutrons

## Slide 109: Formulating Design Requirements Josiah DeLange
Examine previous missions/methods for remote sensing
Define mission goals: locate water, detect gamma rays
Research of basics of current technology
Lots of reading on particle physics
Produce technical summaries (or check datasheets, etc.)
More reading on particle physics

## Slide 110: Engineering Methodology: Photosensors Josiah DeLange
Photoelectric Effect
Convert light into a detectable electronic signal
Photons -----> photo-electrons
Terminology
Photon Detection Efficiency (PDE) - ratio of incident photons to output pulses
Quantum Efficiency (QE) - ratio of photo-electrons to absorbed photons
Available Devices
Photomultiplier tubes [uses photocathode + dynode chain]
Photodiodes [standard semiconductor device]
Silicon photomultipliers [pixelated photodiodes; Geiger mode of operation]
Micro channel plate [“continuous” dynode chain”]

## Slide 111: Refining Design Requirements Josiah DeLange
Scintillation Material Requirements
High efficiency for conversion of excitation energy fluorescent radiation
Transparency to its fluorescent radiation to allow transmission of light
Emission of light in a spectral range detectable for photosensors
Short decay time to allow fast response
Photosensor Requirements
High photon detection efficiency
High quantum efficiency

## Slide 112: Engineering Methodology: High Gain Photosensors Josiah DeLange
R
R
R
R
Dynodes
Anode
High-energy
particle
Scintillator
Photocathode
1 electron
106 electrons
VB
“Dynode Chain” PMT
Notes: Initial electron is accelerated toward first dynode (high bias voltage induces electric field)
Additional electrons produced due to electron avalanche process
Etc; resulting gain of roughly 106
Pros
Ideal for small signals, i.e. single particle detection
Resulting electric signal is sufficiently amplified
Cons
Physical size (larger PMTs require a higher bias voltage)
Sensitivity to magnetic fields
Power requirements

## Slide 113: Engineering Methodology: High Gain Photosensors Josiah DeLange
High-energy
particle
Scintillator
N
P
P+
depletion region
1 electron
106 electrons
Light Pulse
hole
Anode
Cathode
Reflective PTFE tape
Aluminum Housing

## Slide 114: Haley- Lifelong Learning

## Slide 115: Haley- Communication
http://deseng.ryerson.ca/~fil/t/

## Slide 116: Haley- Individual Design Contributions
CubeSat Structure
Followed the standard 6U cubesat shell
  6061-T6 Aluminum
  Total Mass: 10 kg (estimated using SolidWorks)
  Dimensions: approximately 12 cm× 24 cm× 36 cm
Thermal Control
Important in order to keep electronics within their operating temperatures
Multi-Layer Insulation
Thermal Fillers
Verification of Solar Panel absorption and emittance

## Slide 117: Haley- Formulation of Design Requirements
Solar Radiation Intensity
J=P/(4πd2)
J=(3.856 × 1026 W)/(4π×(1.56×1011 m)2)
J=1260.89 W/m2
Temperature at 1.015AU (Full Sun)
J=σT4
T=(J/σ)1/4
T=[(1260.89 W/m2)/(5.6703×10-8 W/m2/K4)]1/4
T= 386.16K = 113°C

## Slide 118: Haley- Formulation of Design Requirements
https://wiki.umn.edu/pub/Asteroid/WebHome/75901_11.pdf
β = 1.1
Equilibrium Temperature and Required Surface Finish
The ratio of absorption versus emittance must be 1.1 for the surface of the CubeSat in order to keep an equilibrium temperature of 25℃.

## Slide 119: Haley- Engineering Methodology
Solar Cell Selection
Based on the β found for the required temperature
Compared multiple solar cell options
Based on the table, a Silicon cell with 3mm glass was chosen
β (Si w/ glass) = 1.1

## Slide 120: Haley- Engineering Methodology
Temperature in Full Sun
with Solar Cells
T ~ 20℃
Variables
α: absorption of solar cells
Fₚ: packing factor of solar array
e: solar cell efficiency
Af: frontal area of solar array
Ab: back area of solar array
Ap: projected area
S: solar constant (1356 W/m^2)
εf: emissivity of front of solar array
εb: emissivity of back of solar array

## Slide 121: Haley-Engineering Methodology
SolidWorks Simulation
3 mm thickness Si layer on outside with ε=0.84 to simply model solar panels
Inside layer modeled with 6061-T6 Aluminum
Surface to ambient radiation
T (Inside): 37℃
T (Outside): 22℃
Challenges were
encountered while trying to
thermally model the entire
CubeSat
Inside of CubeSat
Outside of CubeSat
Modeling Using Simulation Software

## Slide 122: Haley-Engineering Methodology
Multilayer Insulation
Shiny surface reflects radiation while the layers reduce the heat lost
Used research from NASA to select the 15 layers.
As the number of layers increase, the lower the thermal conductivity and emittance
ε = 0.003
MLI is very fragile and could be damaged during launch.
Surface finish under the insulation will be white (low absorption coefficient)
http://matthewwturner.com/uah/IPT2008_summer/baselines/LOW%20Files/Thermal/Spacecraft%20Thermal%20Control%20Handbook/05.pdf