## Slide 1: Socrates
Critical Design Review

## Slide 2: Agenda
    Introduction
    Motivation
    Approach
    Budget
    Design
    Standards
    FMEA
    Conclusion
    Individual Reports
Charlie

## Slide 3: Introduction
Charlie
  Team Lead/Structure
  Charles Denis
ADNCS
Jacob Gustafson
Brian Hanson
Nicholas Sloan
Communications
Ben Setterholm
Tim Kukowski
Power Management
Ethan Arendt
Justin Seifert
Nicholas Janak

## Slide 4: Motivation
SOCRATES,
Charlie D
Signal
Opportunity
Cubesat
Ranging
And
Timing
Experiment
System

## Slide 5: Motivation
Charlie
CONOPS
X

## Slide 6: Motivation
Payload
  Gamma Ray Intensity Detector (GRID)
What GRID does?
  Detect Gamma Ray Events to conceptually prove deep space navigation concepts
Charlie
Figure 1. This figures shows six examples of known Gamma Ray bursts from our universe. The data in the plots represents the relation between Kilo-Electron Volts and Seconds in time.

## Slide 7: Motivation
Requirements
  The CubeSat shall determine and relay a relative position solution (i.e., relative to the formation) with an accuracy of 10 meters (1 standard deviation)
  The CubeSat shall determine and relay a relative attitude solution with an accuracy of 10 mRad.
  The CubeSat shall maintain a clock offset or timing accuracy (relative to the formation) better than 10 µs.
Tim K

## Slide 8: Motivation
Derived Requirements
  Shall accept “GRID” as a payload
    Supplies payload with power (5Whr)
    Communicates with payload (via CAN BUS)
    Provides GRID with environmental data (time, attitude, position)
    Compiles and transmits data from GRID to ground network
  Shall meet NASA CubeSat Launch Initiative requirements
    In appendix
Tim K
X

## Slide 9: Design Approach
Goals
  Successfully carry GRID into LEO
    Subsystems
“Off-the-Shelf”
  Focus on data rather than hardware
  Proven space heritage
  Corporate support for products
Subteams
  Division of labor
Tim K

## Slide 10: Purchases
Flight Computer
GPS
  Reciever Unit
  Antenna
Attitude
  Gyroscopes
  Passive Magnetic Bar
Power
  Power Manangement Board
  Batteries
  Deployable Solar Panels
Radio
  Radio Unit (provided by Aerospace Corp)
  Antenna (Patch)
Structure
  Materials
  Insulation
  Cabling, etc
Jake G.
X

## Slide 11: Budget
Initial Budget
  Lower
    $50,000
  Middle
    $75,000
  Upper
    $100,000
NASA Proposal
Jake G.
X

## Slide 12: Final Budget
Jake G.
Item | Model | Source | Cost
Flight Computer | A712D | GOMSpace | $5,400
GPS receiver | OEM615 | Novatel | $6,000
GPS Antenna | Single Frequency MircoStrip | Antdevco | $5,000
Batteries | NanoPower BPX | GOMSpace | $6,200
Power Management Board | P31us | GOMSpace | $6,200
Radio | MM2-TTL | Freewave | $1,500
Antenna (WHIP)? | CS-CPUT-STX-02 | ClydeSpace | $4,725
Deployable Solar Panels | SP-L-DD1S3U-0039 | ClydeSpace | $40,300*
Gyroscopes | ITG-3050 | InvenSense Inc | $4.73
Final Cost: $80,729
* Denotes the cost of 2
X
Structure, attitude control

## Slide 13: Design - Model
Charlie D

## Slide 14: Design - Structure
Century College to Manufacture to Specifications
  Sub Contracted by UMN
Charlie
X

## Slide 15: Design - Structure
Thermal environment ( heat shielding )
Nick J
X

## Slide 16: Design – Requirements for GRID/GPS
GRID/GPS may generate up to 20 MB per GRB event
GRID/GPS must save data files in 128 KB packets (maximum).
Must use logical data naming structure
Flight computer must generate and save a checksum for each packet file individually
NAME
X

## Slide 17: Design

## Slide 18: Design - Protocols

## Slide 19: Design - ADCNS

## Slide 20: DESIGN - ADNCS Overview
Attitude Determination
  Gyroscope
  Magnetometer
Passive Magnetic Attitude Control
  Pointing Accuracy <5º
GPS
Planned Circular Orbit
  410Km Altitude
  Inclination 60º
Nick S
Notes: SLIDE 19

## Slide 21: DESIGN ADNCS
Passive Magnetic Attitude Control
  Bar Magnet placed within SOCRATES produces torque to align itself with Earth’s magnetic field
  Hysteresis rods damp out oscillatory effects
Why use it?
  Proven space heritage
  No power required
System consists of:
  One 0.3A-m2 bar magnet
  _____ 0.0268T hysteresis rods 95mmx1mm
  All components made from HyMu-80 magnetic alloy
Nick S
Image from Passive Magnetic Attitude Control for CubeSat Spacecraft, Gerhardt and Palo 2010
X
Notes: SLIDE 21, PMAC systems have been successfully used on the University of Michigan’s RAX Cubesat and Colorado’s CSSWE cubesat (Colorado Student Space Weather Experiment)

## Slide 22: Design - ADNCS
System consists of:
  One 0.3A-m2 bar magnet
  _____ 0.0268T hysteresis rods 95mmx1mm
  All components made from HyMu-80 magnetic alloy
Verified in Matlab
  Settling time of ___ days
  GRAPHS HERE
Nick S
X
Notes: SLIDE 22

## Slide 23: Design - ADNCS
Jake G
Orbit
Altitude: 410±100 Km
Inclination: 60±10 Degrees
X
Notes: Moved this slide due referencing STK and orbits before GPS
Orbit uncerinaty is based on testing.
The intial orbit was based on ISS which is shown
However increasing Incliaction gives us more Sunlight time as well as more time, however going over 71 degrees moves us more towards a polar orbit, and then will hurt our sunlight but at 71 it will increase
We could go less Inclination but our data time goes down as well as sunlight time will get smaller, though not by much the Access time will become less and less
As for Altitude we get around the same numbers for adding or subtraction 100km if we go over our Access goes down a lot due to limit range of the Antenna, and going lower 310 we are getting out of leo as its above (220km) however if more is requested we could do more

## Slide 24: Design - ADCNS
GPS (Novatel 615 with Single Frequency MicroStrip)
Output (50 Hz) (Binary)
  GPS Time
  GPS Position and Standard deviation
  GPS velocity and Standard deviation
  Number of Satellites
Space Heritage*
Jake G
* Provided in supplemental material.

## Slide 25: Design - ADCNS
Satellite Verification
  Need 4 satellites
  Verified with STK software
Jake G

## Slide 26: DESIGN ADNCS
Attitude determination
  Generate 2 non-collinear vectors to determine attitude
  Input from gyroscope and magnetometers
High level description
  Integrating angular velocity vector gives position
  However gyro slowly drifts due to bias error which has no bound!!!
  Three axis magnetometer can check accuracy of gyro and “reset” if it drifts too far
Brian H
X

## Slide 27: DESIGN ADNCS
Code Overview
  Read gyroscope data
  Integrate angular velocity
  Determine position
  Compare to magnetometer data
    If too far
      Reset gyro
    Else if gyro data above acceptable bound
      Reset gyro
    End
  Compare gyro data and determine overall attitude
  Repeat
Brian H
X

## Slide 28: Design - Communications

## Slide 29: Design - Communications Overview
Maximum total theoretical data that can be transferred per day: 50 MB
Effects that reduce transfer rate
  Weather
  Communications Algorithm
  Random Data Errors
Expected science data transfer per day: 15 MB
  Based on calculations
Guaranteed total data transfer per day: 10 MB
  Radio data from Aerospace Corp.
Tim K
Notes: Predicted assumes 40% weather throughput, maximum expected data errors, and 1 MB of other data transferred per day (handshakes, diagnostics, log files)

## Slide 30: Design – Communications Algorithm
Ben
Step 1: Active Pinging
Check if any other ground stations are currently in contact with SOCRATES
If not, send hail signal once every 3 seconds

## Slide 31: Design – Communications Algorithm
Ben
Step 2: Establish Connection
SOCRATES replies to hail
SOCRATES transmits GPS location, heading, and velocity information
SOCRATES transmits number of files ready for downlink

## Slide 32: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time

## Slide 33: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time
2°
2000 km

## Slide 34: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time
SOCRATES makes contact
Determine range

## Slide 35: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time
SOCRATES makes contact
Determine range
Forward time step
  3 second intervals

## Slide 36: Design – Communications Algorithm
Ben
Step 4: Command
Ground Station sends command code
  transfer queued file
  transfer log file
  diagnostics
  delete queued file
SOCRATES purges marked files
  delete all data files
  delete log file
  reboot OS
  goodbye

## Slide 37: Design – Communications Algorithm
Ben
Step 5: Transmit Data
SOCRATES transmits one 128 kB packet
  5 time steps
Selective Repeat ARQ (Automatic Repeat Query) protocol

## Slide 38: Design – Communications Algorithm
Ben
Step 6: Error Checking
Ground Station computes checksum
Ground Station transmits checksum

## Slide 39: Design – Communications Algorithm
Ben
Step 7: Confirmation
SOCRATES checks checksum
SOCRATES appends log file
SOCRATES marks file for deletion if transmission successful
SOCRATES relays success/failure to ground station
SOCRATES awaits next command

## Slide 40: Design – Communications Algorithm
Ben
Step 4: Command
Ground Station sends command code
  transfer queued file
  transfer log file
  diagnostics
  delete queued file
SOCRATES purges marked files
  delete all data files
  delete log file
  reboot OS
  goodbye

## Slide 41: Design – Communications Algorithm
Ben
Diagnostics
Onboard Time
GPS Position, Velocity, Satellite Lock
Battery Status, Panel Cell Performance
Attitude Magnetic Lock
Data Storage Check
Detector Diagnostics

## Slide 42: Design - Communications Hardware
FreeWave Radio @ 915MHz
  Compact radio with high data rate
  Receiving radio from Aerospace Corp.
Whip Antenna
  High gain
  Deployable
Tim K
X

## Slide 43: Design - Power
X

## Slide 44: Design – Power
Overview
  Power needed
  Power supplied
  Initial design vs Final design
  Deployables
Justin S
X

## Slide 45: Design – Power
Power Demands:
Component | Power Consumption (Watts)
Payload (GRID) | 5
Flight Computer | 0.33
Magnetometers | 0.06
Gyroscopes | 0.02
GPS Receiver | 0.99
GPS Antenna | 0.3
Radio & Antenna | 0.105 Idle 0.45 Receiving 4.275 Transmitting
EPS | 0.21
Solar Panels | 
Batteries | 0.07
Total | 
Justin S
Battery Operational Range: 77 W – 68 W
Power Supplied Per Orbit: 21.9 W – 7.3 W
X

## Slide 46: Design - Power
Final Design Components
  Power Management Board: P31us – GomSpace
    2 regulated Power buses: 3.3V at 5A and 5V at 4A
    High and low voltage surge protection
    User control of on/off state of bus outputs
    4 operating states dependent on battery voltage
    Measures/Records:
      Current in/out of solar panels
      Battery voltage
      Voltages into output bus & current out of all power output channels
      Temperatures of components
Justin S

## Slide 47: Design - Power
Justin S
Final Design Components
  Batteries: BPx – GomSpace
    8 ion lithium ion cells
    Nominal voltage 12-16.8 V, 5.2 Amps
    Operating power capacity 77 W – 68 W
    Compatible with P31-us EPS board
X

## Slide 48: Design - Power
Final Design Components
Justin S
X

## Slide 49: Design - Power
Enviromental aspects. (orbits)
Nick J
X

## Slide 50: Design - Power
Power order of operations
Nick J
X

## Slide 51: Design – Power Budget
charge vs discharge
Ethan A
X

## Slide 52: FMEA

## Slide 53: FMEA - ADNC
Failure Mode | Mechanism | System Effects | Probability | Severity | Risk Level | Mitigation
Gyroscope status read failure | Mechanical failure, software bug | Accuracy loss of attitude solution | Remote | Minor | Low | Test components before launch. Ensure low vibration during launch.
Tumbling | Passive control on only one axis | Communication problems, unexpected internal forces, insufficient power | Moderate | Critical | Unacceptable | Hysteresis rod control.
Lost position information | Could not get 4 GPS satellite lock | Cannot record position | Extremely unlikely | Critical | High | Moved antenna to point away from earth.
Failure to establish magnetic match | Faulty magnetometer read, damage | Reliance on gyroscope for attitude fix | Remote | Not Relevant | Low | Attitude determination no longer needed for mission. No action
Ben

## Slide 54: FMEA - Communication
Failure Mode | Mechanism | System Effects | Probability | Severity | Risk Level | Mitigation
Radio failure | Electrical short, internal damage | Communication is impossible | Remote | Catastrophic | Unacceptable | Test components before launch. Ensure low vibration during launch.
Hard drive failure | Random chance, internal damage | Data storage and retrieval is impossible | Remote | Catastrophic | Unacceptable | Ensure hard drive is space worthy before launch.
Files get stuck in code loop | Software bug, random glitch | Cannot send next file | Extremely unlikely | Moderate | Low | Command failsafes such as clear buffer, load next file, and reboot OS.
Data Transmission Errors | Atmospheric effects, noise | Incorrect data received | Nearly certain, frequent | Moderate | High | Error checking: Selective Repeat Automatic Repeat Query protocol during transmission, and overall checksum post packet send.
Ben

## Slide 55: FMEA - Power
Failure Mode | Mechanism | System Effects | Probability | Severity | Risk Level | Mitigation
Solar panels fail to deploy | Thermal knife | Not enough power, no mission | Remote | Catastrophic | Unacceptable | None.
Battery underload | Battery failure/dead | No battery power, system only on when solar panels illuminated | Moderate | Moderate | Moderate | Programmed software cases. Report problem in diagnostics.
Battery overload | EPS fails and overloads battery | Explosion | Remote | Catastrophic | Unacceptable | Test component before launch.
Ben

## Slide 56: Conclusion
Delivered:
  SOCRATES Hardware Design
  Planned and Orbit
  Verified Attitude Control
Nick S
X
Notes: SLIDE 49

## Slide 57: What’s next?
Here are the next steps to be done in spring.
  Revisit calculations and designs, revamp etc…
  Final final finalize design.
  Failures etc.
  Build testbeds and verify at high altitude
    GPS
    Attitude Determination
    Powerboard
  HASP Mission in Summer
Brian H
X

## Slide 58
Questions?

## Slide 59: Individual Reports

## Slide 60: Lessons Learned
Things take a lot longer to do than they seem they should
Lot’s of very smart people have already worked out similar problems
  It’s okay to ask questions
  Recycle their ideas
  Open source code is readily available
  Proprietary information is frustrating
  STK makes life a whole lot easier
The atmosphere is a pain
  Data is always available for all frequencies except the one you are working on
Pocket calculator is sometimes more reliable than the code you wrote
  Double/triple check everything
Write stuff down because it’s hard to find again
Ben

## Slide 61: Individual Design Contributions
Communication Hardware
  Initial literature search
Data-Link Budget
  Preliminary Power Calculations
  Data Transmission Error Estimations
  Verification
Orbit Determination
  Altitude and inclination
  Timing study
  Data allowance for GRID
Communication Algorithm
  Studies of existing protocols
  Data management requirements
  Error considerations
    Packet size determination
    Checksum
  Timing estimations
  Algorithm sketch
Ben

## Slide 62: Design – Data Link Budget
Driving Questions:
  Can data be successfully transmitted to Earth?
  How much error can be expected?
Link Budget examines power losses and gains during emission, transmission, and detection of signal
Logarithms make calculations easier
Estimate ground stations at sea level
Ben

## Slide 63: Design – Data Link Budget
Equivalent Isotropic Radiated Power (EIRP)
EIRP (dBW) = Antenna Power (dBW) + Antenna Gain (dB)
For SOCRATES, EIRP = 1.14 dBW
  Power = 1.3 W
  Whip antenna assumed omnidirectional, so gain = 0 dB
Ben

## Slide 64: Design – Data Link Budget
Free Space Losses
Dominant component of losses
Power flux density falls off as 1/r2
Ben

## Slide 65: Design – Data Link Budget
Ben
FSL = 158 dB for link budget calculation

## Slide 66: Design – Data Link Budget
Atmospheric Losses
Ionosphere
  Faraday Rotation - assuming circular polarization, negligible effect
  Scintillation, mid-latitudes (<1 dB)
Ben
Adapted from: Istituto Nazionale di Geofisica e Vulcanologia, Roma2 Department, Aeronomy
URL: http://roma2.rm.ingv.it/en/themes/11/ionospheric_scintillation

## Slide 67: Design – Data Link Budget
Atmospheric Losses
Ionosphere
  Faraday Rotation - assuming circular polarization, negligible effect
  Scintillation, mid-latitudes (<1 dB)
Troposphere
  Extrapolation to 915 MHz
  Zenith attenuation = 0.025 dB
  TLmax = 0.025 dB × csc(2°) = 0.72 dB
Ben
Adapted from: International Telecommunication Union, Recommendation ITU-R P.676-9

## Slide 68: Design – Data Link Budget
Atmospheric Losses
Ionosphere
  Faraday Rotation - assuming circular polarization, negligible effect
  Scintillation, mid-latitudes (<1 dB)
Troposphere
  Extrapolation to 915 MHz
  Zenith attenuation = 0.025 dB
  TLmax = 0.025 dB × csc(2°) = 0.72 dB
Other Losses
  Weather conditions (e.g. rain)
    Depolarization (~2 dB)
    Temporary effects (ignore)
Ben
Total estimated atmospheric loss
AL = 3 dB
Notes: Depolarization ice and rain International Radio Consultative Committee (CCIR)

## Slide 69: Design – Data Link Budget
Pointing Losses
  Off-axis loss at CubeSat
    Dependent on final satellite design, (< 1 dB)
  Off-axis loss at Ground Station
    Generally small (< 1 dB)
  Antenna orientation misalignment
    Depolarization, assuming circular polarized transmission, theoretical max 3 dB.
Ben
Estimated pointing loss
PL = 4 dB

## Slide 70: Design – Data Link Budget
Noise
  Thermal Noise
  Sky Noise
  Ground Noise
NEED TO RE-WORK
Ben

## Slide 71: Design – Data Link Budget
Putting it all together
Ground station signal gain
  AG = 30 dB
Power received at ground station
  Pr = EIRP – FSL – AL – PL + AG
  Pr = 1 dBW – 158 dB – 3 dB – 4 dB + 30 dB = -134 dBW = 40 fW
Ben
Notes: Equivalent Isometric Radiated Power minus propagation losses
GA gain ground antenna 30 dB
Ebno = energy per bit divided by the noise spectral density
B = bits/sec bitrate

## Slide 72: Design – Data Link Budget
Putting it all together
Signal to noise
  Pr = 40 × 10 -15 W
  B = 115 kbps
  kB = 1.381 × 10 -23 J/K
  T = yet to be determined
Bit Error Probability
Ben
Eb/N0 = ?
Pe= Something
Notes: Equivalent Isometric Radiated Power minus propagation losses
GA gain ground antenna 30 dB
Ebno = energy per bit divided by the noise spectral density
B = bits/sec bitrate
Erfc = complimentary error function

## Slide 73: Design – Data Link Budget
Aerospace’s ADV radio and ground network
  Proven downlink 10-15 MB per 24 hour period for LEO satellite (TRL 9)
AsterLabs comparison
  Same operating frequency (914.7 Hz)
  Closed link-budget with 1.2 W antenna at 650 km altitude
  10 MB per 24 hour period
Ben
Notes: TRL – Technology readiness level

## Slide 74: Lessons Learned
don't reinvent the wheel
You can never know too much
Don’t be afraid to ask
  (its okay to not know everything)
Double Check EVERYTHING!!!!!!!!!!!!
Remember to have fun
  But only so much
Jake G
https://trimaps.com/custom-map-users/interactive-map-made-easy-for-developers

## Slide 75: Individual Design Contributions
GPS
  Parts Choice
  Antenna Choice
Attitude determination
  Initial Research on Algorithm
STK
Jake G

## Slide 76: STK
Used for on CubeSat
  Model
  Power Budget
  Link Budget
  GPS Verification
Very Powerful
Not just used for Space Applications
Jake G

## Slide 77: Individual Design Contributions
Attitude determination
  Initial research into hardware
Passive Magnetic Attitude Control System
  Research
  Materials Sourcing
  Matlab simulation and verification
Nick S.
Notes: SLIDE 64, Magnets are annoying.

## Slide 78: Lessons Learned
Importance of Consistency
  Being gone for ~1 month on a 3-month projects makes things difficult
Organization makes your life easier
People want to help (so ask questions)
Space is difficult
Never stop learning
Nick S.
Notes: SLIDE 65, Leaving for Australia took me out of the loop for the project and I had to spend time catching up with where things were. Keeping things together an organized makes things happen. You don’t design in a vacuum. Ask people and you can find help. One paper from our sponsor allowed me to create a matlab simulation to verify our PMACS. Putting something in space makes all of your challenges that much tougher. Orbits, reliability, power; all become really hard when you have zero-margin for failure. I also learned that in space things get hot and cold. I knew that, but never the magnitude of the variation.

## Slide 79
This slide intentionally left blank.