## Slide 1: CubeSat
Critical Design Review

## Slide 2: Agenda
    Introduction
    Motivation
    Approach
    Budget
    Design
    Standards
    FMEA
    Conclusion
Charlie

## Slide 3: Introduction
Charlie
  Team Lead/Structure
  Charles Denis
ADNCS
Jacob Gustafson
Brian Hanson
Nicholas Sloan
Communications
Ben Setterholm
Tim Kukowski
Power Management
Ethan Arendt
Justin Seifert
Nicholas Janak

## Slide 4: Motivation
Charlie

## Slide 5: Motivation
Payload
  Gamma Ray Intensity Detector (GRID)
What GRID does?
  Detect Gamma Ray Events to conceptually prove deep space navigation concepts
Charlie
Figure 1. This figures shows six examples of known Gamma Ray bursts from our universe. The data in the plots represents the relation between Kilo-Electron Volts and Seconds in time.

## Slide 6: Motivation
Requirements
  The CubeSat shall determine and relay a relative position solution (i.e., relative to the formation) with an accuracy of 10 meters (1 standard deviation)
  The CubeSat shall determine and relay a relative attitude solution with an accuracy of 10 mRad.
  The CubeSat shall maintain a clock offset or timing accuracy (relative to the formation) better than 10 µs.
Tim K

## Slide 7: Motivation
Derived Requirements
  Shall accept “GRID” as a payload
    Supplies payload with power (3~5W/hr) and communication requirements
    Provides environmental data (time, attitude, position) to payload with priority
    Receives data from payload to transmit to ground network
  Shall meet NASA CubeSat Launch Initiative requirements
    Structural, electrical, and other requirements are listed at
      http://www.nasa.gov/pdf/627972main_LSP-REQ-317_01A.pdf
Tim K

## Slide 8: Design Approach
Goals
Off the Shelf components
  Why?
  Focus on design, not technology
  Support for components
Subteams
  Divide and conquer
  One to three slides
Tim K

## Slide 9: Purchases
Flight Computer
GPS Antenna
GPS receiver
Batteries
Power Management Board
Radio
Antenna (WHIP)
Deployable Solar Panels
Gyroscopes
Jake G.

## Slide 10: Budget
Initial Budget
  Lower
    $50,000
  Middle
    $75,000
  Upper
    $100,000
NASA Proposal
Jake G.

## Slide 11: Final Budget
Jake G.
Item | Model | Source | Cost
Flight Computer | A712D | GOMSpace | $10,800*
GPS receiver | OEM615 | Novatel | $6,000
GPS Antenna | Single Frequency MircoStrip | Antdevco | $5,000
Batteries | NanoPower BPX | GOMSpace | $6,200
Power Management Board | P31us | GOMSpace | $6,200
Radio | MM2-TTL | Freewave | $1,500
Antenna (WHIP) | CS-CPUT-STX-02 | ClydeSpace | $4,725?
Deployable Solar Panels | SP-L-DD1S3U-0039 | ClydeSpace | $40,300*
Gyroscopes | ? | ? | ?
Final Cost: $80,725
* Denotes the cost of 2

## Slide 12: Design - Model
Solidworks Model HERE
Charlie D

## Slide 13: Design - Structure
Century College to Manufacture to Specifications
  Sub Contracted by UMN
Charlie

## Slide 14: Design - Structure
Thermal environment ( heat shielding )
Charlie

## Slide 15: Design

## Slide 16: Wiring
Jake G
I2C
I2C
Onboard
Onboard
Serial
Serial
CAN
Voltage

## Slide 17: Design - ADNCS

## Slide 18: DESIGN - ADNCS Overview
Attitude Determination
  Gyroscopes
  Magnetometers
Passive Magnetic Attitude Control
  Pointing Accuracy <5º
GPS
Nick S

## Slide 19: Design - ADNCS
Jake G
Orbit
Altitude: 410 Km
Inclination: 60 Degrees
Notes: Moved this slide due referencing STK and orbits before GPS

## Slide 20: DESIGN ADNCS
Passive control mathematatatatatics
why passive?
power savings, etc
FMEA analytics
Nick S

## Slide 21: DESIGN ADNCS
GPS (Novatel 615 with Single Frequency MircoStrip)
Output (50 Hz)
  GPS Time
  GPS Position and Standard deviation
  GPS velocity and Standard deviation
  Number of Satellites
Jake G

## Slide 22: Verification of Satellites
Need 4 satellites
Verification done with STK
Jake G

## Slide 23: DESIGN ADNCS
Attitude determination
High level description, inputs, etc.
Brian H

## Slide 24: Design – Requirements for GRID/GPS

## Slide 25: Design – Requirements for GRID/GPS
GRID/GPS may generate up to 20 MB per GRB event
GRID/GPS must save data files in 128 KB packets (maximum).
Must use logical data naming structure
Flight computer must generate and save a checksum for each packet file individually
NAME

## Slide 26: Design - Communications

## Slide 27: Design - Communications Overview
Maximum total theoretical data that can be transferred per day: 50 MB
Expected effects reducing this value
  Weather
  Communications Algorithm
  Random Data Errors
Expected science data transfer per day: 15 MB
Guaranteed total data transfer per day: 10 MB
NAME
Notes: Predicted assumes 40% weather throughput, maximum expected data errors, and 1 MB of other data transferred per day (handshakes, diagnostics, log files)

## Slide 28: Design - Communications Hardware
FreeWave Radio @ 915MHz
Whip Antenna
TO BE COMPLETED
Tim K

## Slide 29: Design – Communications Algorithm
Ben
Step 1: Active Pinging
Check if any other ground stations are currently in contact with CubeSat
If not, send hail signal once every 3 seconds

## Slide 30: Design – Communications Algorithm
Ben
Step 2: Establish Connection
CubeSat replies to hail
CubeSat transmits GPS location, heading, and velocity information
CubeSat transmits number of files ready for downlink

## Slide 31: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time

## Slide 32: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time
2°
2000 km

## Slide 33: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time
CubeSat makes contact
Determine range

## Slide 34: Design – Communications Algorithm
Ben
Step 3: Computation
Ground station determines communication time
CubeSat makes contact
Determine range
Forward time step
  3 second intervals

## Slide 35: Design – Communications Algorithm
Ben
Step 4: Command
Ground Station sends command code
  transfer queued file
  transfer log file
  diagnostics
  delete queued file
CubeSat purges marked files
  delete all data files
  delete log file
  reboot OS
  goodbye

## Slide 36: Design – Communications Algorithm
Ben
Step 5: Transmit Data
CubeSat transmits one 128 kB packet
  3 time steps

## Slide 37: Design – Communications Algorithm
Ben
Step 6: Error Checking
Ground Station computes checksum
Ground Station transmits checksum

## Slide 38: Design – Communications Algorithm
Ben
Step 7: Confirmation
CubeSat checks checksum
CubeSat relays success/failure to ground station
CubeSat appends log file
CubeSat marks file for deletion

## Slide 39: Design – Communications Algorithm
Ben
Diagnostics
Onboard Time
GPS Position, Velocity, Satellite Lock
Battery Status, Panel Cell Performance
Attitude Magnetic Lock
Data Storage Check
Detector Diagnostics

## Slide 40: Design - Power

## Slide 41: Design – Power
Overview
  Power needed
  Power supplied
  Initial design / needed design
  deployables
Justin S

## Slide 42: Design - Power
Enviromental aspects. (orbits)
Nick J

## Slide 43
Power components
Justin S

## Slide 44: Design – Power Budget
charge vs discharge
Ethan A

## Slide 45: Design - Power
Wiring
Ethan A

## Slide 46: Design - Power
Power order of operations
Nick J

## Slide 47: Design – Power
Nick J

## Slide 48: FMEA
TO BE COMPLETED
Ben S

## Slide 49: Conclusion
Delivered:
  Cubesat Hardware Design
  Planned Orbit
  Verfieid
TO BE COMPLETED
Nick S

## Slide 50: Next steps.
Here is the next steps to be done in spring.
Brian H

## Slide 51: Individual Reports

## Slide 52: Design – Data Link Budget
TO BE COMPLETED
Ben

## Slide 53: Lessons Learned
don't reinvent the wheel
You can never know too much
Don’t be afraid to ask
  (its okay to not know everything)
Double Check EVERYTHING!!!!!!!!!!!!
Remember to have fun
  But only so much
Jake G
https://trimaps.com/custom-map-users/interactive-map-made-easy-for-developers

## Slide 54: Individual Design Contributions
GPS
  Parts Choice
  Antenna Choice
Attitude determination
  Initial Research on Algorithm
STK
Jake G

## Slide 55: STK
Used for on CubeSat
  Model
  Power Budget
  Link Budget
  GPS Verification
Very Powerful
Not just used for Space Applications
Jake G

## Slide 56: Individual Design Contributions
Attitude determination
  Initial research into hardware
Passive Magnetic Attitude Control System
  Materials Sourcing
  Matlab simulation and verification
Nick S.
Notes: Magnets are annoying.

## Slide 57: Lessons Learned
Importance of Consistency
  Being gone for ~1 month on a 3-month projects makes things difficult
Organization makes your life easier
People want to help (so ask questions)
Space is difficult
Never stop learning
Nick S.
Notes: Leaving for Australia took me out of the loop for the project and I had to spend time catching up with where things were. Keeping things together an organized makes things happen. You don’t design in a vacuum. Ask people and you can find help. One paper from our sponsor allowed me to create a matlab simulation to verify our PMACS. Putting something in space makes all of your challenges that much tougher. Orbits, reliability, power; all become really hard when you have zero-margin for failure. I also learned that in space things get hot and cold. I knew that, but never the magnitude of the variation.